## Slide 1
oc_riscv32i
RISC-V RV32I Processor — Complete Explanation
32-bit Datapath
All data 32-bits wide
RV32I ISA
40 instructions
Modular RTL
9 clean Verilog modules
Self-Checking TB
20+ directed tests
This presentation covers:
What it is
How it works
File structure
Worked example
Future: Pipelining
pratik-mhasawade | OpenCores | RV32I Phase 1–3

## Slide 2
What Is This Processor?
The Big Idea
A CPU
A general-purpose computing engine built in Verilog HDL
RISC-V
Open standard ISA — anyone can build a compatible chip
RV32I
The base variant: 32-bit integer instructions, no extensions
Single-cycle
Each instruction completes in exactly 1 clock cycle
OpenCores
Structured for community submission and reuse
Key Numbers
32
bits
Data bus, registers, addresses
32
registers
x0–x31, x0 hardwired to zero
40
instructions
Full RV32I base ISA
9
modules
Clean modular RTL files
4 KB
each
Instruction & Data memory
20+
tests
Self-checking testbench

## Slide 3
Full Datapath — How Data Flows
IF
Fetch
ID
Decode
EX
Execute
MEM
Memory
WB
Writeback
PC
program_counter
IMEM
instr_mem
CTRL
control_unit
IMM
imm_gen
REGS
register_file
ALU
alu
BRU
branch_unit
DMEM
data_mem
WB
WB Mux
pc_next
Fetch Stage
Decode Stage
Execute Stage
Memory Stage
Writeback
Single-cycle: All stages happen combinationally within ONE clock period. On every rising clock edge, PC advances and the next instruction starts.

## Slide 4
File Structure — What Each Module Does
oc_riscv32i.v
[Top-level]
Wires all modules together. Contains all muxes: PC mux, ALU operand muxes, writeback mux. No logic lives here except routing.
program_counter.v
[PC]
32-bit register. Holds current instruction address. Adds 4 every cycle (word stride). Loads jump/branch target when commanded.
instr_mem.v
[IMEM]
4 KB read-only ROM. Async read — instruction is available the same cycle as address. Word-aligned: uses addr[11:2].
control_unit.v
[Control]
Fully combinational decoder. Reads opcode/funct3/funct7, outputs 12 control signals. No clock needed — pure logic.
imm_gen.v
[ImmGen]
Extracts and sign-extends 32-bit immediates from the 32-bit instruction word. Handles all 5 formats: I/S/B/U/J.
register_file.v
[RegFile]
32×32-bit flip-flop array. Two async read ports (rs1, rs2). One sync write port (rd). x0 always returns 0 — hardwired.
alu.v
[ALU]
Combinational. Performs ADD/SUB/AND/OR/XOR/SLL/SRL/SRA/SLT/SLTU. Generates zero flag (branches), negative, overflow flags.
branch_unit.v
[Branch]
Evaluates BEQ/BNE/BLT/BGE/BLTU/BGEU using ALU flags. Outputs branch_taken. Combinational — no clock.
data_mem.v
[DMEM]
4 KB byte-lane RAM. Supports LW/LH/LB/LHU/LBU and SW/SH/SB. Sync read and write. Sign-extends narrow loads automatically.

## Slide 5
Instruction Encoding — How 32 Bits Carry a Command
Every instruction is exactly 32 bits. The bit fields tell hardware WHAT to do, WHERE to read, and WHERE to write.
R-type (register-register) e.g. ADD x4, x1, x2
funct7
31:25
rs2
24:20
rs1
19:15
funct3
14:12
rd
11:7
opcode
6:0
0000000
= normal op
00010
= x2
00001
= x1
00100
= x4
0110011
= R-type
All 5 Instruction Formats at a Glance
R-type
funct7 | rs2 | rs1 | funct3 | rd | opcode
ADD, SUB, AND, OR…
I-type
imm[11:0] | rs1 | funct3 | rd | opcode
ADDI, LW, JALR, SLLI…
S-type
imm[11:5] | rs2 | rs1 | funct3 | imm[4:0] | opcode
SW, SH, SB
B-type
imm[12|10:5] | rs2 | rs1 | funct3 | imm[4:1|11]
BEQ, BNE, BLT, BGE…
U-type
imm[31:12] | rd | opcode
LUI, AUIPC
J-type
imm[20|10:1|11|19:12] | rd | opcode
JAL

## Slide 6
Worked Example — ADD x4, x1, x2 (Step by Step)
Assembly: ADD x4, x1, x2 Meaning: x4 = x1 + x2
Encoding: 0000000 00010 00001 000 00100 0110011 Hex: 0x00208233
1
IF — Fetch
PC outputs 0x04 → IMEM[1] = 0x00208233
The program counter holds the address 0x04. Instruction memory receives this address and immediately outputs the 32-bit word 0x00208233. This is the binary encoding of ADD x4, x1, x2.
2
ID — Decode
Control unit reads opcode=0110011, funct3=000, funct7=0000000
Opcode 0110011 → R-type. funct7+funct3 → ADD. Control asserts: reg_write=1, alu_src=0 (use rs2, not immediate), alu_ctrl=0000 (ADD). Register file reads x1=10, x2=20.
3
EX — Execute
ALU receives operand_a=10, operand_b=20, alu_ctrl=ADD
ALU performs 10 + 20 = 30. Result wire carries 0x0000001E. zero flag = 0 (result is not zero). No branch is taken — pc_src stays 00.
4
MEM — Memory
mem_read=0, mem_write=0 → memory is idle
ADD is not a load or store. Data memory does nothing this cycle. mem_rdata is irrelevant. The ALU result 30 passes straight through the EX/MEM stage toward writeback.
5
WB — Writeback
mem_to_reg=00 → rd_data = alu_result = 30 → x4 ← 30
Writeback mux selects ALU result (not memory). reg_write=1. On the next rising clock edge, register x4 is updated to 30. PC advances to 0x08. Done.

## Slide 7
All 40 RV32I Instructions — Grouped by Function
Arithmetic (R-type)
ADD — x+y
SUB — x-y
SLL — shift left
SRL — shift right (logical)
SRA — shift right (arithmetic)
SLT — signed less than
SLTU — unsigned less than
Logic (R-type)
AND — bitwise AND
OR — bitwise OR
XOR — bitwise XOR
Immediate (I-type)
ADDI, ANDI, ORI, XORI
SLTI, SLTIU
SLLI, SRLI, SRAI
Load / Store
LW, LH, LB — load (word/half/byte)
LHU, LBU — load unsigned
SW, SH, SB — store
Branch
BEQ, BNE — equal/not-equal
BLT, BGE — signed compare
BLTU, BGEU — unsigned compare
Jump
JAL — jump, save return addr
JALR — jump to register+imm
Upper Immediate
LUI — load upper 20 bits
AUIPC — PC + upper imm
System
ECALL — environment call
EBREAK — breakpoint

## Slide 8
Control Signals — The Switches the Control Unit Flips
For every instruction, the control unit reads opcode+funct3+funct7 and sets 12 control signals that configure the datapath:
alu_ctrl[3:0]
Tells ALU which operation to perform (ADD=0000, SUB=0001, AND=0010…)
ADD→0000
alu_src
Selects ALU operand B: 0=use register rs2, 1=use sign-extended immediate
R-type→0, I-type→1
reg_write
1 = write result back to rd in register file. 0 = don't write (store/branch/JAL)
ADD→1, SW→0
mem_read
1 = enable data memory read this cycle (load instructions only)
LW→1, ADD→0
mem_write
1 = enable data memory write this cycle (store instructions only)
SW→1, ADD→0
mem_to_reg[1:0]
Writeback mux: 00=ALU result, 01=memory read data, 10=PC+4 (return address)
ADD→00, LW→01
pc_src[1:0]
PC mux: 00=PC+4, 01=branch target, 10=JAL target, 11=JALR target
ADD→00, JAL→10
branch
1 = this is a branch instruction; enables branch_unit to evaluate condition
BEQ→1, ADD→0
imm_sel[2:0]
Tells imm_gen which format to extract: 000=I, 001=S, 010=B, 011=U, 100=J
LW→000, SW→001
lui_sel
1 = force ALU operand A to zero (LUI: 0 + imm = imm, placed in upper bits)
LUI→1
auipc_sel
1 = force ALU operand A to current PC (AUIPC: PC + upper_imm → rd)
AUIPC→1
mem_size[2:0]
Memory access width (funct3 passthrough): 000=byte, 001=half, 010=word
LW→010, LB→000
Signal
Description
Example

## Slide 9
Why Do We Need a Pipeline? — The Problem With Single-Cycle
The Restaurant Analogy
❌ Single-cycle (current)
One cook does everything alone: takes order → cooks → plates → serves. Next customer waits until the first is COMPLETELY done. Very slow.
✅ Pipelined (future)
4 cooks in assembly line. Cook 1 takes order, Cook 2 starts cooking, Cook 3 plates, Cook 4 serves — ALL simultaneously. 4× more customers/hour.
Processor clock speed is SAME. Throughput is ~5× better.
What Changes in Hardware
Single-cycle clock period
= IF + ID + EX + MEM + WB time
Longest path determines clock. Even NOP wastes full period.
Pipelined clock period
= MAX(one stage time)
Each stage is much shorter. Clock runs 3–5× faster.
IPC improvement
Single: 1 instr / 5 clocks → Pipeline: 1 instr / 1 clock (steady state)
After pipeline fills, one instruction completes every cycle.

## Slide 10
Pipeline Timing — 5 Instructions, 5 Stages, Simultaneously
Single-cycle: 5 instructions take 25 clock cycles | Pipelined: same 5 instructions take only 9 clock cycles
Clk 1
Clk 2
Clk 3
Clk 4
Clk 5
Clk 6
Clk 7
Clk 8
Clk 9
I1: ADD
IF
ID
EX
MEM
WB
I2: LW
IF
ID
EX
MEM
WB
I3: SUB
IF
ID
EX
MEM
WB
I4: BEQ
IF
ID
EX
MEM
WB
I5: SW
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
← All 5
stages
active!
Steady state: from clock 5 onward, one instruction COMPLETES every single clock cycle — this is the power of pipelining.

## Slide 11
Pipeline Hazards — The Problems Pipelining Creates
DATA HAZARD
(RAW — Read After Write)
Fix: Forwarding
Problem: Instruction 2 needs a result that Instruction 1 hasn't finished computing yet.
ADD x1, x2, x3 ← writes x1 in WB (cycle 5)
SUB x4, x1, x5 ← reads x1 in ID (cycle 3) — TOO EARLY!
Solution: Forwarding Unit: bypass the result from EX/MEM stage register directly to ALU input — no stall needed for most cases.
LOAD-USE HAZARD
(Special Data Hazard)
Fix: Stall 1 cycle
Problem: LW result isn't available until end of MEM stage — forwarding alone can't save this one.
LW x1, 0(x2) ← result ready after MEM stage
ADD x3, x1, x4 ← needs x1 in EX stage — 1 cycle too early
Solution: Hazard Detection Unit: inserts 1 stall (bubble/NOP) — freezes PC and IF/ID register for one cycle, gives LW time to finish.
CONTROL HAZARD
(Branch Hazard)
Fix: Flush pipeline
Problem: Processor fetches the next instruction BEFORE it knows if a branch is taken. If taken, the fetched instruction is wrong.
BEQ x1, x2, +16 ← branch condition known at EX
ADD x5, x6, x7 ← already fetched! Wrong if branch taken
Solution: Pipeline Flush: when branch is taken, replace the incorrectly-fetched instruction in IF/ID with a NOP (bubble). 1-cycle penalty.

## Slide 12
Changes Needed — Single-Cycle → Pipelined
1
Add 4 Pipeline Stage Registers
pipeline_regs.v (new)
IF/ID, ID/EX, EX/MEM, MEM/WB registers. Each latches its stage's signals on posedge clk. This is the foundation — without these, nothing else works.
reg [31:0] IF_ID_instr, IF_ID_pc;
reg [31:0] ID_EX_rs1, ID_EX_rs2;
reg [4:0] ID_EX_rd;
reg [3:0] ID_EX_alu_ctrl;
2
Add Forwarding Unit
forwarding_unit.v (new)
Detects when EX/MEM or MEM/WB stage has a result needed by EX stage. Drives 2-bit mux selects (forward_a, forward_b) to bypass register file.
if (EX_MEM_rd == ID_EX_rs1 && EX_MEM_regwrite)
forward_a = 2'b10; // from EX/MEM
else if (MEM_WB_rd == ID_EX_rs1 && MEM_WB_regwrite)
forward_a = 2'b01; // from MEM/WB
3
Add Hazard Detection Unit
hazard_unit.v (new)
Checks for load-use hazards. When detected: stalls PC (hold), stalls IF/ID (hold), zeroes out ID/EX control signals (insert bubble).
if (ID_EX_mem_read &&
(ID_EX_rd == IF_ID_rs1 ||
ID_EX_rd == IF_ID_rs2)) begin
stall = 1'b1; // freeze PC & IF/ID
end
4
Add Branch Flush Logic
oc_riscv32i.v (modify)
When branch_taken=1 at EX stage, flush the IF/ID register by writing NOP (0x00000013). Adds 1-cycle penalty for taken branches.
// In IF/ID always block:
if (flush)
IF_ID_instr <= 32'h0000_0013; // NOP
else
IF_ID_instr <= instruction;
5
Propagate Control Signals Through Stages
control_unit.v (modify)
Control signals generated in ID must travel with the instruction through stage registers: ID→EX (alu_ctrl, reg_write…) → EX→MEM (mem_read, mem_write…) → MEM→WB (reg_write, mem_to_reg).
// ID/EX register carries:
ID_EX_reg_write <= reg_write;
ID_EX_mem_read <= mem_read;
ID_EX_alu_ctrl <= alu_ctrl;

## Slide 13
Summary & What's Next
✅ What Was Built (Phase 1–3)
32-bit single-cycle RV32I processor
All 40 base integer instructions
32 general-purpose registers (x0 hardwired 0)
Full immediate formats (I/S/B/U/J)
Byte/halfword/word memory access
All branch types + JAL + JALR
9 clean, modular Verilog files
Self-checking testbench (20+ tests)
🔲 Upgrade Roadmap
Phase 4 — 5-Stage Pipeline
IF/ID, ID/EX, EX/MEM, MEM/WB regs
Forwarding unit (RAW hazards)
Hazard detect + branch flush
Phase 5 — Cache Hierarchy
L1 I-Cache + D-Cache
Cache controller FSM
Miss penalty handling
Phase 6 — Interrupts / CSR
Trap vector, mepc, mcause
External IRQ lines
FreeRTOS capable
Phase 7 — Wishbone SoC Bus
UART, SPI, I2C peripherals
Address decoder
Full System-on-Chip
github.com/opencore/opencore_for_edu | pratik-mhasawade | LGPL v2.1